Standard Operating Procedure

________________________________________________________

Read the EH&S Standard Operating Procedures Fact Sheet before filling out this form. Print out the completed form and keep a readily accessible hard copy in the lab (also keeping an electronic copy is highly recommended).

______________________________________________________

Date:

SOP Title:  		Sure Seal Bottles

Principal Investigator:

Room and Building:

Lab Phone Number:

Section 1 – Process

Section 2 – Hazardous Chemicals

A variety of chemicals are stored in bottles with sure seals. Such chemicals are highly moisture and/or oxygen sensitive and may react violently with both air and/or water.

Section 3 – Potential Hazards

Chemicals in sure seal bottles may react violently with air and water so it is important to keep them under an inert atmosphere. Additionally, the sure seal on the bottle ensures the state of dryness and thus the purity of the chemical, having impeded its reaction with the atmosphere.

Section 4 – Approvals Required

Use of sure seal bottles requires training and the approval of the appropriate lab member.

Section 5 – Designated Area

Sure seal bottles need to be used in the fume hood with an inert gas line.

Section 6 – Special Handling Procedures and Storage Requirements

Clamp the sure seal bottle to ensure that it will not move. Insert the nitrogen (or other inert gas) needle inlet making sure that the needle is above the surface of the liquid. This will keep the pressure equalized in the bottle during the transfer. Draw inert gas into the syringe being used and flush it out three times to the atmosphere to make sure that there is no oxygen in the syringe. With respect to the needle on the syringe, it must be dry and a larger gauge needle should be used with a larger syringe (but no larger than 18 gauge). Insert the syringe into the sure seal bottle below the surface of the chemical. Holding the needle and syringe together, slowly pull back the plunger, drawing the chemical back into the syringe. Excess chemical can be expelled from the syringe by holding syringe parallel to the bottle, with the needle still inserted in the sure seal. The plunger is then pushed in until the desired volume is in the syringe. The needle is then drawn above the surface of the chemical, still in the bottle under inert atmosphere. The plunger is drawn back again to fill the top of the syringe with inert gas. This will ensure that when the syringe is drawn out the chemical will not accidentally be expelled. The syringe can then be removed from the bottle. As the nitrogen line is removed from the bottle, the sure seal must be covered with Scotch magic tape to cover the holes created by the needles. This will help insure that the bottle remains under an inert atmosphere. See Figure from UCLA SOP www.chemistry.ucla.edu/file-storage/.../SOPLiquidReagents.pdf below.

Section 7 – Personal Protective Equipment

Standard use of a lab coat, gloves, and safety glasses is needed for the use of chemicals in sure seal bottles. The exact PPE will vary depending upon the chemical in use.

Section 8 – Engineering/Ventilation Controls

Work inside the hood and keep the hood sash as low as possible.

Section 9 – Spill and Accident Procedures

The procedure for spill clean up will depend on the specific chemical. See Section 11 – Decontamination and consult other SOP’s and appropriate lab member for more information on the chemical in question before its use.

Section 10 – Waste Disposal

Disposal of chemicals in a sure seal bottle will depend on the specific chemical. Consult other SOP’s and appropriate lab member for more information on the chemical in question.

Section 11 - Decontamination

As with any chemical spill, remove all contaminated clothing, wash all contaminated skin with copious amounts of water. Any further steps for decontamination will depend on the chemical. Consult other SOP’s and appropriate lab member for more information on the chemical in question before its use.